## Slide 1: Power Management System in OSes for IoT
Xiaoyu MIN
EIT ICT Labs Embedded System
Aalto University, School of Science
School of Science
Aalto University
ES Seminar
Cover

## Slide 2: Contents
Importance of EPM in IoT
Application-level EPM
  Android wake lock for Applications
OS-level EPM
  ACPI
  Features in Mobile OS
Hardware EPM
  PMIC (Power Management Integrated Chip)
ES Seminar
Contents

## Slide 3: Need for improved power management
Capabilities of mobile handheld devices improving rapidly:
  Wireless connectivity
  Storage capacity
Battery capacity improving slowly
  I/O devices decrease handheld battery lifetime by 60%
  OEMs provide techniques to reduce battery consumption by severely compromising the performance
  Careful power management needed
ES Seminar
EPM General

## Slide 4: Power Management is essential in IoT Network
Sensor network are often designed for reliable real-time services in IoT
  Limited resource and strict power consumption
  Additional limitation towards some characteristics of conventional OS
Nodes are designed to operate with limited resources
  Power: WSN based use batteries as a power supply
  Memory and operational capabilities: sensing is less resource demanding than computation in conventional OS
Power management is very important in IoT
  Various OS designed for IoT devices: TinyOS, Contiki OS, Android etc..
ES Seminar
EPM General

## Slide 7: Android Wake lock Mechanism
Android implements an application framework on top of the kernel called Android Power Management Applications Framework
The Android PM Framework is like a driver. It is written in Java which connects to Android power driver through JNI
Currently Android only supports screen, keyboard, buttons backlight, and the brightness of screen
Through the framework, user space applications can use ‘PowerManger’ class to control the power state of the device
ES Seminar
Wakelock

## Slide 8: Android Wake lock Mechanism
Notes: By default, Android tries to put the system into a sleep or better a suspend mode as soon as possible
ApplicationsrunningintheDalvikVMcanpreventthesystemfrom entering a sleep or suspend state, i.e. applications can assure that the screen stays on or the CPU stays awake to react quickly to interrupts
The means Android provides for this task is wake locks
If there are no active wake locks, CPU will be turned off
If there are partial wake locks, screen and keyboard will be turned off

## Slide 9: ACPI Specifications
Advanced Configuration and Power Interface (ACPI) specification provides an open standard for device configuration and power management by the operating system.
Power States
  Global states
  Device states
Processor states
Performance states
ES Seminar
ACPI
Notes: First released in December 1996, ACPI defines platform-independent interfaces for hardware discovery, configuration, power management and monitoring. With the intention of replacing Advanced Power Management, the MultiProcessor Specification and the Plug and Play BIOS Specification,[1] the standard brings power management under the control of the operating system, as opposed to the previous BIOS-central system which relied on platform-specific firmware to determine power management and configuration policy.[2] The specification is central to Operating System-directed configuration and Power Management (OSPM), a system implementing ACPI which removes device management responsibilities from legacy firmware interfaces.

## Slide 10: ACPI Specifications
ACPI specification defines the following four Global ‘Gx’ states and six Sleep ‘Sx’ states for an ACPI-compliant computer-system:
Legacy State : The state on an operating system which does not support ACPI. In this state, the hardware and power are not managed via ACPI, effectively disabling ACPI.
G0 (S0)
  Working
  ‘Awaymode’ is a subset of S0, where monitor is off but background tasks are running
G2 (S5), Soft Off
G3, Mechanical Off
  The computer's power has been totally removed via a mechanical switch
ES Seminar
ACPI
Notes: First released in December 1996, ACPI defines platform-independent interfaces for hardware discovery, configuration, power management and monitoring. With the intention of replacing Advanced Power Management, the MultiProcessor Specification and the Plug and Play BIOS Specification,[1] the standard brings power management under the control of the operating system, as opposed to the previous BIOS-central system which relied on platform-specific firmware to determine power management and configuration policy.[2] The specification is central to Operating System-directed configuration and Power Management (OSPM), a system implementing ACPI which removes device management responsibilities from legacy firmware interfaces.

## Slide 11: ACPI Specifications
G1, Sleeping, subdivides into the four states S1 through S4:
  S1 : All processor caches are flushed, and the CPU(s) stop executing instructions. Power to the CPU(s) and RAM is maintained; devices that do not indicate they must remain on may be powered down
  S2: CPU powered off. Dirty cache is flushed to RAM
  S3(mem): Commonly referred to as Standby, Sleep, or Suspend to RAM. RAM remains powered
  S4: Hibernation/Suspend-to-Disk - All content of main memory is saved to non-volatile memory such as a hard drive, and is powered down
ES Seminar
ACPI
Notes: First released in December 1996, ACPI defines platform-independent interfaces for hardware discovery, configuration, power management and monitoring. With the intention of replacing Advanced Power Management, the MultiProcessor Specification and the Plug and Play BIOS Specification,[1] the standard brings power management under the control of the operating system, as opposed to the previous BIOS-central system which relied on platform-specific firmware to determine power management and configuration policy.[2] The specification is central to Operating System-directed configuration and Power Management (OSPM), a system implementing ACPI which removes device management responsibilities from legacy firmware interfaces.

## Slide 12: Linux Energy & Power Management
Notes: System-wide PM
  Global energy-saving states
  Whole system PM transitions
User space decides which energy-saving state to go to and whenRuntime (working state) PM
  User space processes run
  Individual CPU or I/O device energy saving utilized

## Slide 13: Power management for TinyOS & Contiki
TinyOS
  Scheduler responsible for power management
  Power management
    Radio power management
    Managing power of sensor nodes
  Power-Save mode
    Low-power mode (e.g. TinyOS Timer)
Contiki OS
  No standard mechanisms for managing the power state of peripheral devices
  Power optimizations
    Micro-controller in a sleep mode
    Power estimation as additional feature
ES Seminar
EPM for RTOS

## Slide 14: Power management integrated circuit
Power management integrated circuits (power management ICs or PMICs) are integrated circuits (or a system block in a system-on-a-chip device) for managing power requirements of the host system.
A PMIC is often included in battery-operated devices such as mobile phones and portable media players.
A PMIC may include the following parts:
  Battery management
  Voltage regulations
  DC to DC conversion (dynamic voltage scaling)
  Power sequencing
  Miscellaneous functions
ES Seminar
PMIC
Notes: voltage regulation is a measure of change in the voltage magnitude between the sending and receiving end of a component, such as a transmission or distribution line.

## Slide 15: Dynamic frequency scaling
Also known as CPU throttling, whereby the frequency of a microprocessor can be automatically adjusted “on the fly”, either to conserve power or to reduce the amount of heat generated from the chip
Dynamic voltage scaling is another power conservation technique that is often used in conjunction with frequency scaling, as the frequency that a chip may run at is related to the operating voltage.
According to the ACPI Specs, the C0 working state of a modern-day CPU can be divided into the so-called "P"-states (performance states) which allow clock rate reduction and "T"-states (throttling states) which will further throttle down a CPU (but not the actual clock rate) by inserting STPCLK (stop clock) signals and thus omitting duty cycles.

## Slide 16: Power management integrated circuit
Some models feature a low-dropout regulator (LDO), and a real-time clock (RTC) co-operating with a backup battery.
A PMIC can use pulse-frequency modulation (PFM) and pulse-width modulation (PWM). It can use switching amplifier (Class-D electronic amplifier).
Most of the PMIC are integrated with the processor design and they are provided by the chip manufacturers
ES Seminar
PMIC
Notes: voltage regulation is a measure of change in the voltage magnitude between the sending and receiving end of a component, such as a transmission or distribution line.

## Slide 17: Further References
Chameleon: Application Level Power Management with Performance Isolation, Xiaotao Liu, Prashant Shenoy, Mark Corner
Ghosts in the Machine: Interfaces for Better Power Management, Manish anand, Edmund B. Nightngale
Embedded Linux Optimizations, Michael Opdenacker, Thomas Petazzoni, Free Electrons
Android Power Management, Jerrin Shaji George
The Case for Higher-Level Power Management, Carla Schlatter Ellis
Hierarchical Power Management with Application to Scheduling, Peng Rong, Massoud Pedram
Power Management in Mobile Devices, Findlay Shearer
Etc..
ES Seminar
References

## Slide 18
Thank you!